## Slide 1: RISC-V 代码生成
刘先华
2017年12月7日

## Slide 2: ISA：software/hardware interface
Algorithm
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
software
interface
hardware

## Slide 3: RISC-V ISA
RISC design from UC Berkeley
Realistic & complete ISA, but open & simple
Not over-architected for a certain implementation style
Both 32-bit and 64-bit address space variants
  RV32 and RV64
Easy to subset/extend for education/research
  RV32IM, RV32IMA, RV32IMAFD, RV32G
  RV64IM, RV64IMA, RV64IMAFD, RV64G
Technical report with RISC-V spec available on class website or riscv.org
We’ll be using 32-bit RISC-V this semester in labs. Similar to MIPS ISA you saw in course “Computer organization & architecture”.

## Slide 4: RV64 Processor State
Program counter (PC)
32x64-bit integer registers (x0-x31)
x0 always contains a 0
32 floating-point (FP) registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
Is an extension
FP status register (FSR), used for FP rounding mode & exception reporting

## Slide 5: RISC-V Instruction Encoding
Base instruction set (RV32 and RV64) always has fixed 32-bit instructions lowest two bits = 112
All branches and jumps have targets at 16-bit granularity (even in base ISA where all instructions are fixed 32 bits)
  Still will cause a fault if fetching a 32-bit instruction
Notes: 转移和跳转的目的地址都是16位对齐，最后一位地址默认补0
因此，32位指令仍然可能存在非对齐的情况。

## Slide 6: Four Core RISC-V Instruction Formats
Aligned on a four-byte boundary in memory
Sign bit of immediate always on bit 31 of instruction.
Register fields never move
Opcode fields is on the right
Destination Reg.
Source Reg. 2
7-bit opcode field (but low 2 bits =112)
Additional opcode bits/immediate
Source Reg. 1

## Slide 7: With Variants

## Slide 8: I-type
Integer Computational Instructions
ADDI: adds sign extended 12-bit immediate to rs1
All immediate fields in all instructions are sign extended
SLTI(U): set less than immediate
Shift instructions, etc
Notes: SLTIU: Same as SLTI but compares immediate as unsigned.

## Slide 9: R-type
Integer Computational Instructions
Rs1 and rs2 are the source registers. Rd is the destination.
SLT, SLTU: set on less than
SRL, SLL, SRA: shift logical or arithmetic left or right

## Slide 10: S-Type
Compare two registers and branch
  Target address: PC+(immediate<<1)
  Signed offset in multiples of two
  Max branch scope: -4KB ~ +4KB
  Branches do not have delay slot
12-bit signed immediate split across two fields
Notes: 转移和跳转的目的地址都是16位对齐，最后一位地址默认补0
因此，32位指令仍然可能存在非对齐的情况。

## Slide 11: UJ-Type
“J”: Unconditional jump
“JAL”: Jump and link
  Target address: PC + offset<<1
  Max jump scope: ±1MB
  Writes PC+4 to Rd
  If Rd=x1, JAL is used as the function calling
  If Rd=x0, only jump without link

## Slide 12: JALR
uses the I-type encoding
target address: (rs1+offset) <<1
  When rs1=x0, jump to lowest 2KB or highest 2KB from anywhere which could be used to implement fast call to a small routine library.
writes pc+4 to register “rd”
if rd = x1, JALR is used as function calling

## Slide 13: L Type
LUI : Load Upper Immediate
  Writes sign extend 20-bit immediate to top of rd.
  Used to build large immediate number.
12-bit immediates are signed, so have to account for sign when building 32-bit immediates in 2-instruction sequence (LUI high-20b, ADDI low-12b)

## Slide 14: Load and store
Store instructions (S-type), Loads (I-type).
Addressing mode: rs1 + immediate
Store uses rs1 and rs2 but load uses rs1.
Rd is only present when being written to

## Slide 15: Load/Store instruction
LW：load a 32-bit number to register rd from memory
LH： load a 32-bit number to register rd from memory, do 32-bit sign-extension before loading.
LHU： load a 16-bit number to register rd from memory with zero-extension.
LB and LBU are dened analogously for 8-bit values.
The SW, SH, and SB instructions store 32-bit, 16-bit, and 8-bit values

## Slide 16: Where is NOP?
Addi x0, x0, #0
Or define it by yourself
----see pseudo instruction

## Slide 17: Data formats and addressing
Data formats
  8b Bytes, 16b Half words, 32b words and 64b double words
Some issues
  Byte addressing
  Little endian
  Word alignment
0 1 2 3 4 5 6 7

## Slide 18: RISC-V 标准扩展
M集：标准整数乘除扩展，在标准集基础上增加了乘法和除法运算
A集：标准原子指令扩展，使两个处理器间同步原子读，修改和写存储
F集：标准单精度浮点扩展，有浮点的运算和load/store指令
D集：标准双精度浮点扩展，有双精度的运算和load/store指令
Q集：标准四倍精度浮点扩展，有四倍精度的运算和load/store指令
L集：标准十进制浮点扩展，用于64位、128位的浮点运算
C集：标准压缩指令扩展，将32位的指令能与16位的指令相混合
B集：标准位操作扩展，能插入、删除、测试位域
T集：标准面向事务内存（Transactional memory）的扩展
P集：标准Packed-SIMD指令，用于打包的SIMD指令

## Slide 19: “M” Standard Extension
乘法操作
  MUL：实现XLEN-bit*XLEN-bit的乘法，将低XLEN-bit位放在目的寄存器中。
  MULH, MULHU, and MULHSU：将2XLEN-bit位的结果中的高XLEN-bit位放在目的寄存器中。
  要得到相乘结果的高位和低位，推荐的代码顺序：
  MULH[[S]U] rdh, rs1, rs2; MUL rdl, rs1,rs2
    源寄存器说明符顺序一致，rdh不能与rs1或rs2一样。
    微体系结构能把这两条指令融合成一条乘法指令来执行。
  MULW：只对RV64有效，将源寄存器中的数取低32位相乘，将结果的低32位符号扩展后放入目的寄存器中。

## Slide 20: “M” Standard Extension
除法操作
  DIV、DIVU：执行XLEN-bit与XLEN-bit的除法操作，得到商。
  REM、REMU：对除法操作取余数。
  要能同时得到商和余数：
  DIV[U]rdq, rs1, rs2; REM[U] rdr, rs1, rs2
    rdq不能和rs1或rs2一样。
    微体系结构能把这两条指令融合成一条除法指令来执行。
  DIVW、DIVUW：只对RV64有效，将rs1的低32位除以rs2的低32位，将32位的商放置在rd，符号扩展到64位。
  REMW、REMUW：只对RV64有效，将rs1的低32位除以rs2的低32位，将32位的余数放置在rd，符号扩展到64位。

## Slide 21: Divide
除法操作
  对于除0和溢出的情况
  对于除0情况的考虑：
    整数除0：引发异常，会导致触发系统异常。
    浮点除0：设置标志位，写默认值，但不触发异常。
    软件处理除0：每条除法操作都需要加入一条分支指令，这条分支指令通常被预测not taken，会增加一些运行时开销。

## Slide 22: C Datatypes for RISC-V ISA

## Slide 23: Assembler Mnemonics

## Slide 24: Calling Conventions
The RISC-V calling convention passes arguments in registers when possible. Up to eight integer registers, a0–a7, and up to eight floating-point registers, fa0–fa7, are used for this purpose.
In the standard RISC-V calling convention, the stack grows downward and the stack pointer is always kept 16-byte aligned.
We don’t care about float types.

## Slide 25: 运行目标码
在操作系统（虚拟机？）上运行
  将汇编代码转换为二进制代码
  初始化
  链接
在模拟器（更高层次的虚拟机）上运行
  便于调试
  移植性好

## Slide 26: 本阶段任务
将任意给定的符合 MiniC 规范的源码正确地翻译为 “符合 RISC-V 规范的代码”
主要挑战：栈的安排
  本帧的运行栈应该多大（空间优化）？
  如何多用寄存器、减少内存访问（时间优化）？
  选择哪个指令？

## Slide 27: “我的编译器我做主”
在保证运行结果正确的前提下
实现上有充分的自由
例如：运行栈中
每帧的内容可以自己确定
不一定完全按照例子的模式
“高效”与“易维”
每个人有不同的体会
最后都可以写到《实习报告》

## Slide 28: 实现本次任务的基本途径
1）彻底理解RISC-V指令系统及运行机理
  运用相关课程讲的 RISC-V 知识
2）进一步扩展自己的程序，使其能将已生成的中间代码进一步转换为 RISC-V 代码
  回顾“目标代码生成”内容
  参考《现代编译器的Java实现》第11、10章
3）合并前面所有步骤，成为“一个完整的编译器”
而不是“多个分步骤的编译器”！

## Slide 29: 什么时候结束？
如何判断自己的编译器是否正确？
  运行自己的编译器，将一个正确的 MiniC程序翻译为 RISC-V 代码
  利用 模拟器 执行生成的代码
  看运行结果是否与Mini-C程序应运行结果相同
有精力的同学可以进一步 做活性分析、优化代码
提高执行速度
降低内存消耗
提高编译器的实用性

## Slide 30: 实习报告撰写
刘先华

## Slide 31: 报告内容（参考框架）
一、编译器概述
1、基本功能
2、自己所开发编译器的特点
二、编译器设计
1、概要设计（图+文字解释）
1）模块结构
2）模块内的类图（哪些类、属性、方法）
2、详细设计（自己的特色）
1）算法
2）符号表
3）类型检查

## Slide 32
三、编译器实现
1、对工具软件的介绍
1）功能
2）自己的看法
2、各个阶段的编码细节
1）关键功能
2）具体实现方法
选择该方法的原因
可以包含必要的代码
3）编码难点

## Slide 33
3、测试
  1）测试用例构造
  2）测试效果
    a) 测出过哪些主要的错误
    c) 怎么发现的（发生错误的条件）
    b) 怎么解决的
4、发现课程所使用的工具中存在的问题
  1) lex/yacc
  2) Eeyore 解释器
  3) Tigger 解释器
  5) 模拟器

## Slide 34
四、实习总结
1、收获与体会
1）主要的收获是什么
2）学习过程的难点是什么
2、对课程的建议
1）实习过程优化的建议
2）实习内容的建议
3）对老师讲解内容与方式的建议

## Slide 35: 如何提交报告?
一般20-30页A4
时间：2018年1月14日北京时间23:59前
方式：电子版
发给：
  gaozheng@mprc.pku.edu.cn
  taomiao@mprc.pku.edu.cn
  liuxianhua@pku.edu.cn